## Slide 1: Understanding Internet Protocols
TCP vs. UDP Key Differences, Pros, and Cons
WAMS-MCC Software Training Meeting
J. Ritchie Carroll
Dec 3, 2024

## Slide 2: Where in the Stack?
TRANSPORT: TCP / UDP (Internet Protocols)
  Foundational Base Layer
DATA: IEEE C37.118 / IEEE 2664/STTP (Synchrophasor Protocols)
  Data Transfer Layer
APPLICATION: PDC functions / Archiving Functions (openHistorian Tools)
  User Operation Layer

## Slide 3: Introduction to TCP and UDP
TCP (Transmission Control Protocol) and UDP (User Datagram Protocol) are the two, most common, fundamental communication protocols of the Internet.
Used for transmitting data between devices, each has unique features and use cases.

## Slide 4: Internet Protocols Operate with “Packets”
Networks are inherently unreliable, packet delivery is not guaranteed
A block of data is sent in “packets”
Packet sizes, called Maximum Transmission Units (MTU), are controlled by routers,
  Smallest size wins (commonly 8K)

## Slide 5: What is TCP?
Connection-oriented protocol
Ensures reliable data delivery
Uses error checking and retransmission
Data is sent in sequence, ensuring order
Example Use Cases: Web browsing, email

## Slide 6: What is UDP?
Connectionless protocol
Faster but less reliable than TCP
No error checking or retransmission
Ideal for real-time data transfer
Example Use Cases: Online gaming, video streaming

## Slide 7: Key Differences Between TCP and UDP
Reliability
  TCP: Reliable (error-checking and retransmissions)
  UDP: Unreliable (no guarantees)
Speed
  TCP: Slower due to overhead
  UDP: Faster for real-time use
Connection
  TCP: Connection-oriented
  UDP: Connectionless

## Slide 8: Pros and Cons of TCP
✅ Reliable data transfer
✅ Ensures data arrives in order
✅ Error-checking and retransmissions
❌ Slower due to overhead
❌ More resource-intensive
❌ Retransmission delays

## Slide 9: Pros and Cons of UDP
✅ Faster transmission
✅ Low overhead
✅ Ideal for real-time applications
❌ No guarantees of delivery
❌ No error-checking
❌ No retransmissions