## Slide 1: Understanding PDC's / openHistorian
PDCs and openHistorian Overview / Details
WAMS-MCC Software Training Meeting
J. Ritchie Carroll
Dec 3, 2024

## Slide 2: Where in the Stack?
TRANSPORT: TCP / UDP (Internet Protocols)
  Foundational Base Layer
DATA: IEEE C37.118 / IEEE 2664/STTP (Synchrophasor Protocols)
  Data Transfer Layer
APPLICATION: PDC functions / Archiving Functions (openHistorian Tools)
  User Operation Layer

## Slide 3: PDC’s Introduction
Brief overview of a PDC and its importance in power systems.

## Slide 4: Primary Function: Data Routing / Distribution
Phasor Data Sharing
PDC has a Data Distribution Role
Introduction

## Slide 5: Focus on Measurements
Numeric quantities that have been acquired at a source device are often known as points, signals, events, or time-series values. For the openPDC, these are known as measurements:
    Examples include: temperature, voltage, vibration, location, luminosity and phasors
The openPDC is “Measurement Centric”
Other PDCs typically manage data a “Frame” level, i.e., a timestamp followed by associated values
Introduction

## Slide 6: Streaming Data Processing
Most time-series processing engines operate on archived static data
PDC’s operate on moving time-series data, as it streams by, acting as a streaming data processing engine:
openPDC has an extensible adapter architecture for processing streaming data distinguishes it from other commercial PDCs
Introduction

## Slide 7: Supported Protocols
Traditional
  IEEE C37.118-2005  #1 in popularity
  IEEE C37.118.2-2011
  IEC 61850-90-5
  BPA PDCstream
  IEEE 1344-1995
  SEL Fast Message
  Macrodyne Protocol
  F-NET (UTK) Protocol
New
  Streaming Telemetry Transport Protocol (STTP) / IEEE 2664-2024
  Predecessor: Gateway Exchange Protocol (GEP)
Introduction

## Slide 8: Adapter Based
Introduction

## Slide 9: Adapter Type Functions
Inputs
  Accommodates multiple inputs from PMUs and PDCs
  Parses the inputs, gracefully handing input anomalies
Actions
  Aligns the data based on time-stamp during a configurable waiting period
Outputs
  Produces a real-time stream of output data, e.g., to an archive
Introduction

## Slide 10: Action Adapter: Time Alignment
Device 1
Device 2
Device 3
Near by
Far
Synchronized
Measurements
Max Lag Time
Introduction

## Slide 11: Included: Computational Adapters
Introduction

## Slide 12: Included: Dynamic Calculator Adapters
Introduction

## Slide 13: Primary Components

## Slide 14: openHistorian Introduction
Overview of openHistorian and its role in data archiving and analysis.

## Slide 15: Primary Function: Data Archiving / Extraction
Phasor Data Sharing
Historian has a Data Archive Role
Introduction

## Slide 16: Core Engine: SNAPdb
Serialized
NoSQL
ACID Compliant
Performant
Introduction
https://github.com/snapdb
Latest code in development for .NET Core available on GitHub:

## Slide 17: What is ACID?
SNAPdb Implements ACID to protect data integrity:
  Atomicity - requires that database modifications must follow an "all or nothing" rule. Each transaction is said to be atomic
  Consistency - ensures that any transaction the database performs will take it from one consistent state to another
  Isolation - refers to the requirement that no transaction should be able to interfere with another transaction at all
  Durability - that once a transaction has been committed, it will remain so
Introduction

## Slide 18: Components
API allows adapters to be developed for data inputs
Recent data served with very low latency from memory
High performance data storage with lossless data compression
Tools provided for historical data extraction
Both publish / subscribe and web services interfaces
Companion tools allow users to view and export data
Introduction

## Slide 19: openHistorian is Adapter Based
Introduction

## Slide 20: System Components
STTP Pub/Sub
Protocol Parsers
Configuration
Administrator's Console
openHistorian Information Insight Excel Plug-In
openHistorian Manager
Custom Adapters
.d2 File Reader
Bulk Data Extraction
periodically
Read Cache
Write Cache
Intermediate Files
SERVER
SNAPdb SDK
Web Services
openHistorian API
ARCHIVER
Output Adapter
Interfaces
KVP Data Store
Introduction
openHistorian implements SNAPdb as an Output Adapter

## Slide 21: SNAPdb Data Structure
B+Tree based file structure that supports out of sequence insertion
Time support to +/- 100 nanoseconds (ticks) (with extended time precision fields available)
Data can be of any type that can fit in 192-bits (for example, float32, float64, complex32, complex64, int32, int64, uint32, uint64, char and string16)
Data stored sequentially in compressed 4K structures
Tested and optimized for phasor data
Introduction

## Slide 22: Key-Value Pair Structure
Key is an identifier, e.g., join of PointID and Time
Value is data, for openHistorian, up to 192-bits*
Default KVP structure for the openHistorian:
Value
Key
64 bits
64 bits
64 bits
64 bits
64 bits
64 bits
Point ID
Ticks**
Ext Prec.
Time Flags
Quality Flags
DATA
* 192-bits is used by the openHistorian as the size of values and keys – this is not a restriction of the SNAPdb. SNAPdb can work with any Key / Value structure definition.
**1 Tick = 100 nanoseconds
Time Flags = duplicate entry counter (for DST), leap second, etc.
The 64-bit PointID is used internally and not normally referenced at the user level. Rather a GUID is assigned through configuration as well as primary and alias Tags.
10 Bytes V1
48 Bytes V2
(unencoded)
Introduction

## Slide 23: B+ Tree Overview
Tree grows from the bottom up
Leaf-nodes contain blocks of sequential data
Nodes are doubly linked and point to previous and next node
Tree indices are unsigned 32-bit integers which require internal-nodes to support large trees
Introduction

## Slide 24: SNAPdb B+ Tree Specifics
The leaf node of data is encoded and decoded dynamically to optimize memory and storage
Implementation operates directly from disk without requiring an in-memory data structure
The data encoding process is used to implement lossless data compression
Introduction

## Slide 25: .D2 File Format
Version #
Node Level
Node Structure
Record Count
Bytes Used
1 Byte
1 Byte
2 Bytes
2 Bytes
Left Sibling
4 Bytes
Right Sibling
Lower Key
Upper Key
Data Block
4 Bytes
24 Bytes
24 Bytes
4096 Bytes
Footer Block
32 Bytes
The .D2 file contains a table of contents, a B+Tree header and nodes: a root node, internal nodes and leaf nodes:
Introduction

## Slide 26: .D2 File Layout
Data Block (in blue) is a B+Tree Collection of 4K Leaf Nodes
Introduction

## Slide 27: .D2 File Creation
Real-time – Recent data cache (in memory)
Stage 1 – Flushes real-time cache to disk (10 second default)
Stage 2 – Consolidates Stage 1 files (created based on either size or time constraints)
Stage 3 – Create final .d2 archive file (created based on size constraints)
Temporary Archive Files
Final Archive
_________________________________________________________________________
Recommended size 2GB
Introduction

## Slide 28: System Configuration
Setting up openHistorian for optimal performance.

## Slide 29: Tools
Adapter Explorer
APP PDC Importer
Archive Comparison Utility*
Archive Upgrade Utility*
Bulk Calculation State Manager
Configuration Encryption Utility
XML Configuration Editor
CSV Output Stream Creation Tool
CSV SQL Configuration Data Manager (Import / Export / Update)
Data Migration Utility
DNP3 Configuration Generator
Data Extraction Utility
System Configuration
Historian Playback Utility
Statistic Archive Historian Trend / View Tool
Log File Viewer
Macrodyne Device Controller
No Internet Configuration Utility
openHistorian (Service)
openHistorian Console
openHistorian Manger
openVision Tool*
SEL PDC Importer
Statistics Report Generation Tool
Update COMTRADE Counters Web Utility*
Update Tag Name Expression Utility
* Tool unique to openHistorian

## Slide 30: User Interfaces
Use Desktop Manager for:
  Adding new devices
  Managing custom adapters
  General system configuration
  Common monitoring
Use Web UI for:
  Association of currents to voltages
  Application of dynamic calculations (tag templates)
  User / Group management
  Data trending and export
Desktop vs. Web UI

## Slide 31: Console Access: Diagnostics / Config Verification
Access Options
  Application: “C:\Program Files\openHistorian\openHistorianConsole.exe”
  Desktop Manager
  Web UI
Console App

## Slide 32: Historical Data Retrieval
Accessing and downloading historical data for analysis.

## Slide 33: Web UI Data Extraction
Historical Data Retrieval

## Slide 34: Data Extraction Utility
Historical Data Retrieval

## Slide 35: openHistorian includes Grafana (https://grafana.com/)
Open source
Rapidly expanding library of graphical widgets
Tutorials on-line (YouTube)
Displays easily shared and modified
Extensible
Data integrated across multiple domains
GPA published plug-ins for openHistorian and PI
The open platform for beautiful analytics and monitoring
Version 5.2
https://grafana.com
https://www.youtube.com/watch?v=1cRWVMw5U-c&t=610s
( for a demo)

## Slide 36: Standard Display Plugins
Clock
Pie charts
Alert List
Lists of links (to other dashboards)
Graphs – line, bar, area, etc.
Heatmap
Single stat
Tables
Markdown Text

## Slide 37: System Status Dashboard

## Slide 38: Contributed Display Plugins
Gauges
Traffic Lights
Annotated Diagrams
State vs. Time Panel
Geo-Loop Heat Maps
User Interaction
Plot.ly
Radar Charts
Data overlay on pics
Status Dot (SSAM)

## Slide 39: System Monitor Dashboard

## Slide 40: NOC Dashboard Example