## Slide 1: GPA Proposal Discussion – Part 1
Opening Remarks
Application Demonstration
Russell Robertson & Ritchie Carroll November 28, 2017
Notes: Thank everyone – honored to be here to tell our story, especially since we have no visualization product per se.
Point 1 – We’re focused on your REQUIREMENTS
So, we’re going to start with Into (blasting through)

## Slide 2: GPA Proposal – Opening Remarks
About GPA & T&D Consulting
Proposal Technical Approach
Proposal Business Approach
Part 1
November 28, 2017
Notes: Move briskly
… Going to be blasting through the intro

## Slide 3: Grid Protection Alliance
Mission – to improve the reliability and resiliency of the electric grid
Purpose – to advance the technology of the electric grid by providing software and software services that create lasting value for electric energy producers, transmission & distribution companies, and consumers.
GPA is a not-for-profit corporation formed to facilitate the development of comprehensive electric energy solutions.
https://gridprotectionalliance.org
Part 1
November 28, 2017
Notes: Started in late 2009 – Along with the announcement of the smart grid investment grants.
Our impact has been greater than anticipated.

## Slide 4: Key GPA Staff
Russell Robertson
Vice President, Grid Solutions
ROLE: Overall Project Oversight
Founded GPA’s open-source software and consulting-service business.
30+ years at the Tennessee Valley Authority, last 10 leading TVA OT – including all information systems that support RC, BA, IA, TOPs and TO functions.
Expertise in grid operations, IT/OT architecture, information management, and control systems.
Concurrently with GPA responsibilities, Director of Grid Data Management in 2014 for the CURENT center at the University of Tennessee.
Grid Protection Alliance, Inc., specializes in the development and support of innovative software solutions for the electric industry.
GPA has a track record of innovation and has led major software development projects with client utilities and the Federal Government.
In addition to custom application development, GPA offers services for installation, set-up, integration, and on-going maintenance of its open-source software.
Oversees GPA software development and provides software system design and development services to utilities.
25+ years’ expertise in high-performance software system design, development, and delivery. Has lead numerous large software development projects.
10 years at the Tennessee Valley Authority leading synchrophasor software development among other operational systems
Active participant in NASPI and other industry efforts to improve synchrophasor data systems.
Major contributor to GPA software solutions and provides system support and integration services to utilities.
10 years’ experience in developing .NET solutions, much of that time contributing significantly to GPA’s core code base – the Grid Solutions Framework.
Specialize in the management of data from substation devices – PMUs, DFRs, power quality meters, and relays.
Prior to joining GPA, 2 years’ experience at the Tennessee Valley Authority in development of synchrophasor data software.
Provides project management and technical writing support.
30+ years at the Tennessee Valley Authority, serving in a variety of roles including the management of R&D projects, developing corporate performance metrics, and participating in corporate power system planning and corporate strategy efforts.
Expertise in project management, strategic planning, and environmental, energy, and natural resource management.
Ritchie Carroll
Senior Solutions Architect
ROLE: Lead Developer / Architect
Richard Driggans
Senior Project Manager
ROLE: Project Management Support
Stephen Wills
Senior Systems Analyst
ROLE: Senior Developer
Specializes in user interfaces/user experience, data storage, data visualization, and full-stack Web development.
Experienced with numerous front end development JavaScript APIs including AngularJS, ReactJS, KnockoutJS, among others
Lead developer on the Open PQ Dashboard with two years of experience at GPA developing .NET and web-based solutions
Billy Ernest
System Analyst
ROLE: Developer
Part 1
November 28, 2017
Notes: We’re a small company. Around 10 employees – and we do scale up and down with business.

## Slide 5: T&D Consulting Engineers
Role:
  To actively participate in the specification/initial development stage to ensure ease-of-use and ability to interpret results for the proposed WASA system;
  To provide guidance in specifying, and quality control in fulfilling, the desired outcomes in each of the 24 specific use cases identified in Appendix C of the RFP;
  To generally augment the core GPA software team with additional domain expertise and guidance.
T&D Consulting Engineers is a small consultancy with domain expertise in synchrophasor deployments and power system dynamics, and with knowledge of western grid policies, procedures and issues.
Part 1
November 28, 2017
Notes: Over to Matt

## Slide 6: T&D Consulting Engineers’ Subject Matter Experts
TDCE provides domain expertise in measurement systems and signal processing, synchrophasor applications, and power system operations.
Staffed by highly qualified technical professionals, TDCE brings an in-depth understanding of signals and systems applied to power engineering along with the ability to effectively communicate this knowledge through documentation and training.
Dan Trudnowski, PhD, PE
Managing Partner
ROLE: Engineering SME
IEEE Fellow “for contributions to algorithms for characterizing power-system small-signal stability properties.”
Over 90 refereed publications over entire career; IEEE PES prize paper awards, 2009, 2013.
25+ years investigating the dynamics of the western North American power grid; regular contributor to JSIS subcommittee of WECC.
Acting Dean of the College of Engineering at Montana Tech.
Matt Donnelly, PhD, PE
Managing Partner ROLE: Engineering SME
30+ years in power systems and power engineering with special expertise in measurement systems.
Convener of NASPI predecessor and contributor to NASPI, JSIS and SMS efforts.
Active participant in NASPI and other industry efforts to improve synchrophasor data systems.
Josh Wold, PhD
Staff Engineer ROLE: Engineering SME
Expert in mathematical modeling with current research interest in power plant model validation (conventional and renewable).
Hardware engineer at Schweitzer Engineering Lab prior to joining TDCE and Montana Tech.
Part 1
November 28, 2017

## Slide 7: An Architecture of Component Reuse
GPA products are light weight and leverage the functionality provided by the GSF – which contains the large majority of GPA’s open source code.
GPA quickly incorporates the latest updates/revisions from Microsoft to take advantage of performance and security improvements. (Now using .NET 4.6.1)
GPA libraries are tested on multiple platforms (Windows, Linux, Mac) to assure wide use
Part 1
November 28, 2017
Notes: Now a quick intro on the technology
Again, move very quickly
Products are light, GSF heavy
We track updates from Microsoft closely
We test on multiple platforms

## Slide 8: GPA Software is Open Source
Posted on Github
  44 Repositories
Permissive Licensing
Nightly builds available on-line from GPA
GPA is an active code steward
Code Security
  Checked at development time
  Checked nightly using SolarQube
Part 1
November 28, 2017
Notes: So that’s the “Who” – Now a quick intro on the “What”

## Slide 9: GPA Core Technology
Grid Solutions Framework
Time-Series Library
A comprehensive collection of classes and methods useful for any project
Foundational code library for all GPA products with 100’s of class libraries
860,000 lines of code and more than 225,000 lines of comments spanning more than 75 assemblies
Version 2.2.144
Part 1
November 28, 2017
Notes: GSF is the core.

## Slide 10: No Data Loss, ~40% Less Bandwidth
Data Loss
2.12
0.14
IEEE C37.118
GEP
UDP
UDP
UDP
TCP
TCP
Large
Large
Medium
Medium
Small
0.22
0.0
0.31
0.04
0.03
0.0
0.12
0.02
Bandwidth UDP (MBITS/S)
IEEE C37.118
GEP
UDP
UDP
UDP
TCP
TCP
Large
Large
Medium
Medium
Small
2.71
4.95
2.77
1.58
0.89
0.89
0.15
0.08
1.72
0.60
See: Link for Full Report
Part 1
November 28, 2017

## Slide 11: SDG&E is a Participant in the DOE ASP Project Lead by GPA
Low-Level API
Applications
Applications
Provided by the ASP Project
STTP Commands
STTP Commands
Low-Level API
The Wire Protocol
Performant Data Exchange at Scale
Extensible Metadata
Access Control and Security
Bidirectional Connectivity
DOE FOA 1492
DE-OE0000859
Part 1
November 28, 2017
Notes: We’re well into the development of a new protocol that builds upon GEP

## Slide 12: GPA’s Disturbance Monitoring Tool Suite
Part 1
November 28, 2017
Notes: I do what to mention our disturbance tool suite – that fully automates the process of downloading and analyzing DFR data
Only what you want
Used most by TVA, SOCO & GTC.
Development largely sponsored by EPRI
openXDA is the core.
Includes analytics – all 5 IEEE single ended fault location methods, plus doubled ended.
Breaker timing

## Slide 13: Open PQ Dashboard
The display layer for openXDA data
Drill-down from wide-area data displays all the way to waveforms
Complements traditional vendor-provided waveform analysis tools
Ability to manually override automated results and add notes
Recent Improvements
Features
Version 2.0
Part 1
November 28, 2017

## Slide 14: GPA’s Synchrophasor Product Suite
Copyright © 2014, Grid Protection Alliance, Inc. All Rights Reserved.
Collect
Distribute
Analyze
Save
Display
Part 1
November 28, 2017
Notes: I believe you know most of our products …

## Slide 15: GPA Leveraged Technology
Open source
High performance
Well-documented APIs
Supports both map and non-map base layers
Extensible
ESRI provides a tile layer for Leaflet
an open-source JavaScript library for mobile-friendly interactive maps
Version 1.2.0
http://leafletjs.com
https://github.com/Esri/esri-leaflet
Part 1
November 28, 2017

## Slide 16: GPA Leveraged Technology
Open source
GPA published plug-ins for openHistorian and PI
Rapidly expanding library of graphical widgets
Displays easily shared
Extensible
The open platform for beautiful analytics and monitoring
Version 4.6
https://grafana.com
Part 1
November 28, 2017

## Slide 17: 30+ Grafana Display Panels are Available
Part 1
November 28, 2017
Gauge
Trending Chart
Heat Map
Pie Chart
Diagram
Alarm
Time
Stacked Trending
Status Panel
Notes: For display of data, it can be superior to what’s available in your EMS.
Seamless RT & Historical data.

## Slide 18: GPA Solution Typical Architecture
* Connection established from the higher security zone
Commercial Historian
Test Systems
Field Devices
External
High Security
Field
Enterprise
C37.118
Perf. Hist.
GEP*
Perf. Hist.
Failover Cluster
DQ Reports
DMZ
GEP*
Other Applications
Adv. Tools
Adv. Tools
Phasor Fault Detection
Vendor Analytics
Extensible Control & Analytics
Integrated Analytics
Extended
Part 1
November 28, 2017
C37.118
(GPA’s version of RFP Attachment 4, Figure 4, page 12)
Notes: To wrap up technical approach intro
Go over quickly – don’t see PDQTracker on this list – why because the openPDC is the swiss army knife – we push all almost all functions there.

## Slide 19: The GPA Business Approach
Minimizes first and on-going costs
Performant and flexible architecture
Adaptable to meet changing business requirements without vendor lock in
Delivery is in phases to return value early
The proposal team has the skills and experience to be successful
Leverage existing open source software
Develop new open source software to close function and feature gaps
Test and document
Part 1
November 28, 2017
Notes: Cost, Performance, Flexibility

## Slide 20: Application Demonstrations
Trending Data Displays
“Mapped Data” Displays
Alarming
Building New Displays
Adding New Analytics
Configuration
Q&A
Part 1
November 28, 2017

## Slide 21: GPA Solution Functionality – Trending Data Displays
Grafana Data Sources
Grafana Dashboard
  SPP Example
  ODM Example
Demo – TVA Phasor Data Monitor
Part 1
November 28, 2017

## Slide 22: Grafana Data Sources
Browser
Server Side Systems
openHistorian (~ 25 mSec Latency)
GSF Performance Historian(s)
  openPDC
  SIEGate
  …
OSI-PI
STTP / Real-time (Futre)
Data source, filters and functions
Saved Dashboards
Plugins
Part 1
November 28, 2017

## Slide 23: openHistorian Data Source -- Built-in Functions
Average
Minimum
Maximum
Total
Range
Count
Distinct
Absolute Value
Add
Multiply
Round
Floor
Ceiling
Truncate
Standard Deviation
Median
Mode
Top
Bottom
Random
First
Last
Percentile
Difference
Time Difference
Derivative
Time Integration
Interval
Include Range
Exclude Range
Filter NaN
Unwrap Angle
Wrap Angle
Label
Subtract
Divide
36 & Growing
Part 1
November 28, 2017

## Slide 24: Trending Data Displays – Grafana Dashboard, SPP
Frequency
ACE
Load
Generation (Wind Generation)
Interchange
Time
Part 1
November 28, 2017

## Slide 25: Trending Data Displays – Grafana Dashboard, SPP
2-Axis
  Control Limit
  Load
  Load % of ATC
2-Axis
  Frequency
  ACE
Load and Generation
Part 1
November 28, 2017

## Slide 26: Trending Data Displays – Grafana Dashboard, SPP
Generation Mix
  Mixed bar and line
  Values and legend
  Donut (current mix)
Part 1
November 28, 2017

## Slide 27: Trending Data Displays – T&D Oscillation Detection
2-Axis
  Energy
  Bad Data
15 minute window
5 second refresh
Oscillation Bands
  Band 1 – 0.0 to 0.1 Hz
  Band 2 – 0.1 to 1 Hz
  Band 3 – 1 to 5 Hz
  Band 4 – 5 Hz and Up
Part 1
November 28, 2017

## Slide 28: Trending Data Displays – Grafana Data Monitor
Display developed to monitor phasor data flow availability for TVA
Connected to SDG&E test data for demonstration
Demo will show:
  Connecting to data sources
  Using openHistorian time-series data functions
  Speed of data load
  Ease of adjustment of time scales
  Ability to set local alarms
A display to monitor data availability.
Part 1
November 28, 2017
Notes: A

## Slide 29: GPA Solution Functionality – “Mapped Data” Displays
Demo – Phase Angle Difference Monitoring
Demo – Over an Image
Demo – Gradient Display / Map Overlay
Part 1
November 28, 2017
Notes: Just experiments … What to build what you need and want.
However, we thought it would be good to perform some experiments.

## Slide 30: Developing a New Grafana Plugin -- Leveraging Leaflet
Experiment to explore techniques and level of difficulty
Widget consists of:
  Value phase angle
  Value magnitude
  Min and max angle for the displayed time window
Leverages native Leaflet “lines”
The “Polar Widget” Design
Min & Max angle for the time window
Angle @ (t)
Core size proportional
to magnitude
Color indicates
angle alarm state (not implemented)
Positioned Geospatially
Using Leaflet
Configurable Size
Part 1
November 28, 2017
  Effort
  300 lines of TypeScript (compiled down to JavaScript)
  About 2 days to develop and test

## Slide 31: “Mapped Data” Displays – Phase Angle Difference Monitoring
Used Leaflet and new “polar widget”
Demo will show:
  Ability to build custom Grafana panel with configurable options.
  Geospatial display with zooming
  Options for multiple map base layers
  Drill down to more detail
Part 1
November 28, 2017
A display to monitor angle differences.

## Slide 32: “Mapped Data” Displays – Overlay Data on Image
Data can be displayed over images – in this case a single line diagram
Demo will show:
  Superimposed data over an image with fast refresh
Note: GPA has researched building SCADA like HMIs (substation schematics) as a Grafana panel. We believe that highly functional displays can be built that meet SDG&E’s requirements.
Part 1
November 28, 2017

## Slide 33: “Mapped Data” Displays – Map Overlays
Map overlays via Leaflet
ESRI provides a tile layer for Leaflet
Demo will show:
  df/dt on a gradient display
  Ability to zoom and pan the map display
  Addition of a weather layer
Part 1
November 28, 2017
A display to highlight frequency change.

## Slide 34: GPA Solution Functionality - Alarming
Standard Alarming
New “Advanced Tools” Alarming
Alarm Management
RFP Requirements vs. GPA Proposal
Part 1
November 28, 2017

## Slide 35: GPA Standard Alarming
Full featured alarming service in use since 2011
Includes
  Delay
  Hysteresis
Part 1
November 28, 2017

## Slide 36: Enhanced Data Quality and Range Flags Carried with Data
Bad Data Flags
  Time
  Data
  Unreasonable Outside engineering possibility
  Latched
  … and more
Data Range Flags
  Standard Control Chart
    Warning
    Alarm
  Implausible
As identified by the PMU
&
Part 1
November 28, 2017
Notes: Computed as early as possible on raw values and used for all downstream operations.
High value in not having to test for bad values over and over.

## Slide 37: Advanced Alarm Generation – For Example, Oscillation
Advanced alarms can be derived from multiple other values and/or alarms
Advanced alarms can be based on more complex alarming criteria.
Advanced alarms can include suppression logic.
Advanced Alarming
Inverse-time alarm
Alarm Distribution
Event Repository
Event
Management
Part 1
November 28, 2017

## Slide 38: Atypical (off-normal) Alarming
Simple learning required
  Histogram of minute-of-week data
Data science techniques could yield higher value
Atypical pattern
Advanced Alarming
Part 1
November 28, 2017

## Slide 39: Alarming Vision
Alarms – Something that requires operator attention and action
Alarms can be raised from events from multiple tools and systems
A single system manages the operator interface
Event Generation
Event Distribution
Alarm Repository
Alarm
Management
Part 1
November 28, 2017
ISA 18.2
Notes: - The alarm type
– The alarm class
– The alarm priority (based on rules in the alarm philosophy)
– Alarm limit or condition
– Required operator action
– Consequences of not carrying out operator action in a timely manner
Frequency Monitor†
Frequency Deviation Alarms †
Phase Angle Reference Monitor †
Phase Angle Difference Alarms †
Real Power Monitor †
Voltage Monitor †
Reactive Power Monitor †
Voltage Stability Monitor* †
Oscillation Monitor* †

## Slide 40: RFP Requirements vs. GPA Proposal
Multiple Outputs
GUI(s) Configurable
System Flexibility
Drill to substation schematic
Display in tables
Operator Acknowledgement
Suppress nuisance alarms
Notes: Objective: Timely Decision Making
  Holistic view of alarm data
  Reduction in alarm overload & noise
  Improve awareness in rationalizing alarms
Automated email notifications
Alarm suppression logic
Mobile access
Easy access to alarm history
Alarms can originate from multiple sources
AOR Alarm Groups
Acknowledgement can be required
Tools to allow operators to bulk clear alarms following major events
Includes Advanced Alarming

## Slide 41: Key Features
Objective: Timely Decision Making
  Holistic view of alarm data
  Reduction in alarm overload & noise
  Improve awareness in rationalizing alarms
Automated email notifications
Alarm suppression logic
Mobile access
Easy access to alarm history
Alarms can originate from multiple sources
AOR Alarm Groups
Acknowledgement can be required
Tools to allow operators to bulk clear alarms following major events
Includes Advanced Alarming
Part 1
November 28, 2017
Notes: Alarm class -- ?? Options voltage level, local or requires distribution
Alarm types – Critical, Alarm, Warning, Info
Alarm states – Raised (Unacknowledged), Acknowledged, Cleared, Return-to-Normal, Shelved, Blocked
Alarm message --
Operator annotations – Ack Comment
Why? Typical – Low, High plus a broad range of others.

## Slide 42: Managed Alarms vs. Convenience Alarms
Managed Alarms
Registered as “events” in the Event Repository
Must be acknowledged to cleared
  Manually
  Automatically
Assigned an AOR
Full auditability via a relational data base.
Basis for Phasor SOE
Convenience Alarms
Not registered as “events”
Set by individual user as watch points based on temporal operating conditions
Implemented within the dashboard itself via Grafana panels
Part 1
November 28, 2017

## Slide 43: GPA Solution Functionality - Building New Displays
Demo – Building a frequency disturbance monitor
Part 1
November 28, 2017

## Slide 44: Frequency Disturbance Monitor Requirements (for Demo)
Based on frequencies from each substation – each with a primary and one or more back-up measurement sources. Alert if primary is not available.
Alarm if average frequency is outside 50 mHz control band from nominal
Alarm if any frequency deviates by more than 20 mHz vs. a 5 second rolling average.
Show alarm clearly on the display
Part 1
November 28, 2017
Notes: Make the observation – That the screen came together quickly. Even for the experiment – it fostered lots of discussion about HOW the data should best be displayed.
Synchronized Controls
Annotations
Frequency Monitor†
Frequency Deviation Alarms †
Phase Angle Reference Monitor †
Phase Angle Difference Alarms †
Real Power Monitor †
Voltage Monitor †
Reactive Power Monitor †
Voltage Stability Monitor* †
Oscillation Monitor* †

## Slide 45: Frequency Disturbance Panel – Data Flow
Bad Data Flagging
Set high bits
Freq 1
Freq 2
Freq 3
Freq 4
Freq 5
Freq 20
Good Value Selector
10 Freq’s
Average Frequency
Dynamic Calculator
Frequency
Disturbance
Adapter
Set
Low bits
SAVED VALUES
Set
Low bits
  Up to 20 Freq’s
  Average Freq
  Min
  Max
  Alarm State
Can be implemented in the openPDC, SIEGate or openHistorian
  For each of 20
    Primary
    Backup(s)
    None (all bad)
+/- 20 mHz
+/- 50 mHz
60 Hz
over 5 Sec
Event
db
Part 1
November 28, 2017
Substation Freq

## Slide 46: Solution Functionality – Adding New Analytics
Introduction to openECA
Demo – building a new analytic from scratch
Part 1
November 28, 2017
Notes: High value point
Where rubber meets the road

## Slide 47: Analytic Functionality – Introduction to openECA
DOE FOA 970
DE-OE-778
  Lowers cost of addition of new production analytic tools
  Simplified end-to-end configuration and change management
  Improved availability of phasor data with greater visibility of phasor data quality
  Robust scalable solution to support phasor data infrastructure of any size
  Complements existing phasor data architectures and supports integration with other data sources such as SCADA
Part 1
November 28, 2017
Notes: e.g., detection of very high impedance faults.

## Slide 48: Linear State Estimator (Kevin Jones)
Features
Architecture:
  Easy to use installation package
  Deployable as a real-time service.
  Directly integrated with openECA.
Tools: Modeling and Offline Analysis Tool
  Automated model build & measurement mapping
    Model Schemas: GE-Alstom, PSSEv33, and expanding
  Integration with openECA for automated meta-data creation
  Integrated measurement sampler for offline testing
  Single and batch offline analysis, reports
Visualization: Out-of-the-box Grafana dashboards for trending of Input, Output, Performance Metrics
Docs: Wiki contains walkthrough for all procedures
Service, Installers: https://github.com/kdjones/openLSE
Core Libraries: https://github.com/kdjones/lse
LSE Performance Metrics shown in Grafana
Integrated Modeling and Offline Analysis Tool
Part 1
November 28, 2017

## Slide 49: Linear State Estimator (Kevin Jones)
Features
Architecture:
  Easy to use installation package
  Deployable as a real-time service.
  Directly integrated with openECA.
Tools: Modeling and Offline Analysis Tool
  Automated model build & measurement mapping
    Model Schemas: GE-Alstom, PSSEv33, and expanding
  Integration with openECA for automated meta-data creation
  Integrated measurement sampler for offline testing
  Single and batch offline analysis, reports
Visualization: Out-of-the-box Grafana dashboards for trending of Input, Output, Performance Metrics
Docs: Wiki contains walkthrough for all procedures
Advantages over other LSEs
Performs estimation with or without breaker status telemetry
Completely open source software
Interoperability through openECA
Positive Sequence and Three Phase Estimator
Native Intel MKL Linear Algebra Providers
Automatically disables input measurement chatter
Multiple output data types:
  flows, residuals, breaker statuses, validation flags, metrics, etc.
Supported with domain expertise and active development
Service, Installers: https://github.com/kdjones/openLSE
Core Libraries: https://github.com/kdjones/lse
Part 1
November 28, 2017

## Slide 50: openECA – DOE Project Provided Analytics
Real-Time Analytics
  Oscillation Detection Monitor (ODM)
  Oscillation Mode Meter (OMM)
  Topology Estimation
Control
  Regional Volt-Ampere-Reactive (VAR) Control
  Local VAR Control
  PMU Synchroscope
Off-Line Analytics
  Dynamic PMU Transducer Calibration (Automated, Periodic Use Case)
  Line Parameter Estimation (Ad-Hoc Use Case)
  Synchronous Machine Parameter Estimation (Research Use Case)
  Acceleration Trend Relay (ATR) Improvement (Research Use Case)
Plus: Linear State Estimation
Open source
Proprietary
DOE FOA 970
DE-OE-778
Part 1
November 28, 2017
Notes: Be sure and reference the rest of the morning and the poster sessions.

## Slide 51: T&D Domain Expertise Will Be Applied To Analytics
Development of analytics related to 24 use cases from Appendix C of RFP
Specification and QC for visualization widgets related to “custom” analytics (i.e. those analytics that are more sophisticated than built-in functions)
Testing, training and refinement of analytics and visualization widgets
Part 1
November 28, 2017

## Slide 52: Demonstration – Building and deploying a new analytic
Standard Deviation of Power
Oscillation detection “on the cheap”
openECA
Analytic
VØ(t)
IØ(t)
STDev( |MW| )(t)
30 sps – Moving 15 second window
Part 1
November 28, 2017

## Slide 53: openECA – Process for Building an Analytic
Part 1
November 28, 2017

## Slide 54: Managing Configuration
Metadata Management
Configuration Management Tools
Part 1
November 28, 2017

## Slide 55: Meta Data Management
Metadata dynamically exchanged via GEP
Modeled after C37.118 signal  phasor  device  location
Extensible
Patterns for metadata management currently being debated within the STTP project
Part 1
November 28, 2017

## Slide 56: Configuration Management Tools
openPDC/SIEGate/openHistorian Manager
  Add a PMU / Add a signal
  Apply security settings
  Monitor application status
Console provide low-level system diagnostics
Configuration Utility
  Installation
  Switch configurations (e.g., promote test to production)
Part 1
November 28, 2017

## Slide 57: Application Demonstration – Additional Questions ?
Part 1
November 28, 2017