## Slide 1: GPA Proposal Discussion – Part 2
Solution Architecture
Solution Delivery
Russell Robertson & Ritchie Carroll November 28, 2017

## Slide 2: GPA Solution – Typical Architecture
* Connection can only be established from the higher security zone
Commercial Historian
Test Systems
Field Devices
External
High Security
Field
Enterprise
C37.118
Perf. Hist.
GEP*
Perf. Hist.
Failover Cluster
DQ Reports
DMZ
GEP*
Other Applications
Adv. Tools
Adv. Tools
Phasor Fault Detection
Vendor Analytics
Extensible Control & Analytics
Integrated Analytics
(with Metadata management in Pi-AF)
Part 2
November 28, 2017
Extended
Metadata
Data
C37.118
Notes: I’ve shown you this before – I’ve added the metadata flow to this one.
We understand that this will need to be mapped onto your existing architecture..

## Slide 3: SDG&E High-Level Data Flows
Metadata
Field Devices
Perf. Hist.
C37.118
Commercial Historian
Perf. Hist.
C37.118
*Streams replicated from each substation
*
Field
Enterprise
External
SCADA/EMS
Test Systems
C37.118
Phasor
Adv. Tools
Extensible Control & Analytics
Integrated Analytics
Vendor Tools
C37.118
Other Applications
Part 2
November 28, 2017
(Adaptation of Figure 1, page 8 in RFP Attachment 4)
Notes: Since most any GAP component can provide almost all functionality, the product names in the boxes don’t have too much meaning. However, there are some gaps to close in this architecture.
(1) SIEGate that designed to be isolate in a DMZ with low attack surface and minimum functionality – provides the SDG&E centralalized real-time data distribution service (what the openPDC was designed to do best). -- It along with the stream splitter is are the most critical components in the architecture.
The historian provides the same functionality between the two architecutres– with about the same data flows. However, the SDG&E architecture also requires the historian to perform concentration via the way it saves data. Not a real time concentrator. SOLUTION – A data flow from the PDC in GEP to the openHistorian.
Our most powerful software, the openPDC is a just a protocol converter.
Short story. This can work – and we’ll be happy to implement just this way. However, it very likely that improvements can be make to this architecture that will (1) reduce overall network loading, (2) make the system intrinsically more robust, (3) improve security and (4) improve the interoperability of systems.

## Slide 4: GPA Solution – Architecture
Security
Logging
Integration Approach
Scalability
Part 2
November 28, 2017

## Slide 5: Solution Architecture -- Security Requirement Gaps
CIP Compliant Design
Autonomously Secure
Consistency
Active Directory Integration
Role Based Security
Audit Logging
Authorization Controls
Secure baseline configuration
Cryptographic Key Management
Information input validation
Supports Periodic Backup
Can be monitored
Least functionality
Malicious Code Protection
Password strength enforcement
Encrypts stored data
Part 2
November 28, 2017

## Slide 6: GPA Patch and Code Review Assurance
Enables compliance with CIP standards. FIPS support.
Products quickly migrated to latest .NET libraries
Numerous utility code checks
Third Party (largely Microsoft) security patches applied within 30 days.
Visual Studio’s built-in code analysis applied during build process
SolarQube used to perform static code analysis monthly
  All products
  All code libraries
Part 2
November 28, 2017

## Slide 7: Solution Architecture – Logging
Late data
Event logging
Configuration change logging
Log viewing/filtering
User cannot modify
Error logging
Programmatic wrapper for APIs
Annunciation panel key 24x7 cyber SA tool
“Bubbles” below are systems – each containing many data flows
Successful data flows are logged
Each data flow: - Has an expected periodicity, or execution time - Is linked to dependencies on hardware e.g., server names, subnets
For the Visualization Layer
Grafana utilizes log15, a “best practice” logger
Part 2
November 28, 2017
Notes: System Status and Alarm Monitor – TVA 2002  2005

## Slide 8: Solution Architecture – Integration Approach
GPA products are open source and built with multiple points of integration including APIs and Web Services.
GPA is proficient in the many of the major programming languages (C, C++ Java, Python, C#, among others) and data base systems (Oracle, MS SQL Server, MySQL, SQLite, among others) as deployed on both Linux and Windows platforms and has developed multiple interfaces with third party systems.
There are only a few integration gaps between SDG&E architecture and the GPA solution – the largest being using PI as the master metadata source.
Part 2
November 28, 2017
Notes: Ritchie to speak to how we flip that.
GE XA/21 EMS (via OSI-PI)
OSI-PI
ESRI Base Maps (via – Leaflet)
openECA analytics
Third party analytics

## Slide 9: Solution Architecture – Scalability
All GPA products are scalable to many millions of points per second on pedestrian hardware – and are typically horizontally scalable beyond that.
GPA has not yet extensively stress tested Grafana; however, indications are that it will scale well with the infrastructure.
GPA prides itself on delivering high-performant solutions that dynamically scales to the number of cores and memory presented to it.
Part 2
November 28, 2017

## Slide 10: Solution Architecture – Additional Questions ?
Part 2
November 28, 2017

## Slide 11: GPA Solution – Delivery
Approach & Schedule
Graphical Requirements Gaps
Data Migration
Development Approach
Testing & Acceptance
Part 2
November 28, 2017

## Slide 12: The Proposal Timeline (Revised)
2 to 4 Months
Develop the VSS Design Document
Define the precise scope of each phase
Turn-up test and acceptance systems
Begin prototyping key displays
Future
Provide on-going product maintenance
Design
12 Months
Develop VSS functionality for Beta Release
Install in acceptance
Conduct SAT
Conduct training
Deploy pre-production
Pre-Production
Phase 1
12 Months
Production
Integrate with additional systems
Develop balance of VSS functionality
Conduct SAT
Conduct training
Deploy in Production
Phase 2
Part 2
November 28, 2017

## Slide 13: Three Major Development Groups
Adv. Tools
Adv. Tools
Part 2
November 28, 2017
Extended
Metadata
Data

## Slide 14: Advanced Tools
Metadata Integration with Pi-AF
Batch configuration tools
  Alarm settings import & export
  PMU locations
  Assignment of name aliases
Fully implement bad data and data range flagging in GSF
Crisp integration with Alarm Management System
Part 2
November 28, 2017

## Slide 15: Alarm Management System
SCADA-like alarm management capability
Can launch with limited functionality
Includes advanced alarming service
[ See Part 1, Slide 42 for a list of openAMS features. ]
Advanced Alarming
Part 2
November 28, 2017
a.k.a. Notification Engine

## Slide 16: Grafana Displays
Major focus of the Design Document
Prototype displays and test with operators / engineers using existing Grafana panels in acceptance - e.g., frequency disturbance, real power, voltage
Build displays that require development of new panels – e.g., system/substation schematics
Extended
Part 2
November 28, 2017
Notes: Frequency Monitor†
Frequency Deviation Alarms †
Phase Angle Reference Monitor †
Phase Angle Difference Alarms †
Real Power Monitor †
Voltage Monitor †
Reactive Power Monitor †
Voltage Stability Monitor* †
Oscillation Monitor* †

## Slide 17: With greater understanding, less estimated effort and cost.
As Proposed
5th Ten
3rd Ten
Next 25
2nd Ten
Top Ten
Estimated hours – Sorted by Effort
Development Hours
Development costs can be estimated with greater precision following creation of the Design Document.
Part 2
November 28, 2017
Notes: Fully understand the importance of operationalizing – e.g., How does the tool need to be reset on shift change? What’s retained, what’s not.
No “dimensional” data base as cache
Use of ESRI base maps easier
Total development hours – 8,694
Top 10
1 Synchronized Displays - 640
2 Annotations – 640
3 Saving Displays – 320
4 DFR Integration – 320 (I bet it’s ½ that)
5 X-Y Charting – 320
6 All aspects configurable – 240
7 Multi-page and multi-tab visualization – 240
8 Switch between auto scaling and fixed scaling – 240
9 Bar chart grouped by forecasted, scheduled, actual -- 240
10 Nomograms – 240
(There are 10 items @ 240 hrs – 5 above)

## Slide 18: Solution Delivery – Data Migration
No data migration will be required from SDG&E existing solution.
Part 2
November 28, 2017

## Slide 19: Solution Delivery – Development Approach
Responding to change > Following a plan
Client collaboration > Structured development process
Robust, highly-performant software > Comprehensive documentation
There is high-value on the right; however, GPA values the left more.
Phase OBJECTIVES
Phase Function & Feature Blocks
Develop (in the open)
Bench Test
Deploy in Acceptance
Refine
Document
For each block
Phase Completion
Comprehensive SAT
Correct defects
Pre-production deployment
Correct defects
Production deployment
[ adapted from Microsoft ]
Part 2
November 28, 2017

## Slide 20: Solution Delivery – Display Development
Be consistent
Put data in context to enhance understanding
  Show trends
Match the user’s mental/work model
Make important information stand out
Minimize cognitive load
  Keep it simple
  Use color and motion sparingly
  Dials and other analog representations preferred over digitals
Provide information (not data) and group information that belongs together
Where possible, provide operating boundaries on displays
Create an information hierarchy – from overview information down to the details
Part 2
November 28, 2017

## Slide 21: Solution Delivery – Testing & Acceptance
Bench testing in GPA’s Offices
Early installation in SDG&E acceptance
Frequent SDG&E acceptance updates
Formal SAT
Bench testing in GPA’s Offices
Frequent SDG&E acceptance updates
Formal SAT
Production Installation
Phase 1
Phase 2
No FAT Necessary
Part 2
November 28, 2017

## Slide 22: The GPA Proposal - Approach
Minimizes first and on-going costs
Performant and flexible architecture
Adaptable to meet changing business requirements without vendor lock in
Delivery is in phases to return value early
The proposal team has the skills and experience to be successful
Leverage existing open source software
Develop new open source software to close function and feature gaps
Test and document
Part 2
November 28, 2017
Notes: In our presentation today, we’re going to touch on our response to your RFP from time-to-time. Everything we talking about is congruent with the proposal – including the approach. Shown here. If you re-read this summary you’ll see that the touchstones are cost, performance, flexibility, phased delivery and out ability to successfully meet your requirements.
In the proposal we also have a section on business value – summarized here. As you know – we don’t have a product where our mission today would be to convince you to buy this product – even though it’s old and even though it doesn’t quite meet all your requirements. Our proposal is “less create exactly what you need.”
This slide is also the closest we’re going to get to “sales” in our presentation today. We don’t have a marketing department, or a regional sales manager – nor do we have sales targets nor have we broken down your RFP to look for our greatest profit opportunities. Now I’m not faulting others that do this work – if I were managing a big company with many opportunities I’d be sure to use methods to find the most profitable engagements – and my pricing would be market-based. I’m just saying it’s not something we do.
So what’s our motivation, aren’t you here to make money you say. Yes, we are definitely here to sell you services – and in doing so we’re looking to (1) advance our portfolio of open source offerings and (2) add value to the industry – framed contextually by the items you see here. Cost – performance – flexibility.
We’re a small company – tiny really. We give away our products under a permissive, open source license. And we have a reputation(we think – but you can be the better judge of this) for creating products that are well architected and designed to perform well at scale.
So that’s the introduction – Cost, Performance, Flexibility. From this point forward we’re excited to be talking you about “what we propose”. We’ve done some quick prototyping over the past several weeks. It’s been fun for us. We hope that you like what you see.

## Slide 23: Business Basis for Selecting GPA
Value at the pace of investment
Precisely meets business requirements
Low total cost
High quality
Start-of-the-art
Assured security
Fast delivery
Future Proof
  Low cost of modification
  Can incorporate best-of-breed technology
No vendor lock-in
Enables innovation
Lowers Risk
  Scalability
  Technology
  Business
Strategic
Tactical
Part 1
November 28, 2017

## Slide 24: Solution Delivery – Additional Questions ?
Part 2
November 28, 2017