## Slide 1: The openPDC Project
October 7, 2009

## Slide 2: Source Code Status
TVA’s SuperPDC has been in production use since early 2005.
The source code is based on .NET 3.5 and written almost exclusively in managed C#.
The code set has over 300,000 lines of fully documented code spanning 630+ classes.
Includes detailed API help files for the source code.
Everything needed to create your own operational PDC is included in the code.

## Slide 3: What’s Included…
The TVA Code Library: this consists of code for handling sockets, threading, error management, security, etc. as well as basic data concentration and archival and general phasor protocol parsing / generation.
The openPDC synchrophasor projects: these include all the SPDC components (IAON host and adapter layer, phasor protocol adapters, etc.), the PMU Connection Tester and…
A working experimental prototype implementation of NASPInet to spur further development and discussion.

## Slide 4: What’s not included…
Generally TVA has provided all the available source code related to its SPDC; however there are certain pieces of code that we cannot release.
No source code will be released for the following:
  TVA’s DatAWare Historian System
  The NERC funded PCS Software*
  Other internal TVA System Software
* The NERC PCS is built on top of the openPDC.

## Slide 5: Where do I get the code?
You can download the all the source code and/or pre-compiled installation packages from the following URL:
http://openpdc.codeplex.com
Any public contributions consisting of new features, updates or fixes will be accepted by TVA. However, all contributions will first be reviewed for security and completeness before they are integrated with the public code. Attributions to contributors will remain in the code.

## Slide 6: High Level System Overview

## Slide 7: Third Party Integration Options
Out of the box the system can accept streaming data from IEEE C37.118 (version 1 and draft 6), BPA PDCstream, IEEE 1344, F-NET, SEL Fast Message and Macrodyne*.
The system can also generate a concentrated outgoing stream of either IEEE C37.118 or BPA PDCstream.
Additionally, the SPDC exists as a layered “plug-in” architecture and can be easily extended with new “assemblies” (a.k.a., DLL’s) to handle real-time calculations, data exports, or new protocols.
* Macrodyne protocol is in beta testing.

## Slide 8: Layered Plug-in Architecture
NASPInet Subscriber
NASPInet Publisher